## Slide 1: EE G13 Presentation
Group members
Honu Seraphine Elorm
Kwadwo Boadu Ayeboafo
Atakora Elisha
Forson Stephen Ekow
Don Jullian Yartey
Tiboore Sampson Kaara Yiri

## Slide 2: Table of Contents
Problem Statements
Methodology
Demonstration/Simulation
Conclusion

## Slide 3: Problem Statements
This project is designed to test the time it takes for one to react to led(in this case blue and ) using an Arduino-based system where the user must press the corresponding button as quickly as possible.
The system records the reaction time and displays it on an LCD screen. If the user presses the wrong button, it notifies them. This project can be useful for training reflexes, improving response speed, or just as a fun game.

## Slide 4: Methodology
1. Setup the Components – Connect an Arduino to an LCD screen, two LEDs (blue and green), and two buttons.
2. Initialize the System – The Arduino turns off all LEDs and displays "Wait..." on the LCD.
3. Random LED Activation – After a random delay (2–5 seconds), one LED turns on.
4. User Response – The player must press the button matching the LED.
5. Reaction Time Measurement – If correct, the LCD shows the reaction time in milliseconds. If wrong, it shows "Wrong Button!".
6. Restart the Game – After a short delay, the game resets for another round.

## Slide 5: Demonstration
The project was tested using TinkerCAD, a virtual Arduino simulator. The video presentation would entail the presentation better

## Slide 6: Conclusion
The project run as expected the LEDs came on randomly the LCD displayed the appopriate time in milliseconds the push buttons were set to the pullup method which deployed the internal resistance of the Arduino microcontroller hence no external external resistance was required.
The projects could help diagnose the receptiveness of ADHD patients ,It could help to train drivers to be more receptive to traffic lights
We could add buzzers and a multiplayer support and when required to be used as game